Wireless Module
Yuxiao Tan

---
General Information
General Information
There are two boards involved in Car to Pit data transmission.
- Mainboard
- Wireless board (integrated into main board)

---
General Information
General Information
Mainboard:
- Very powerful, but drains battery heavily(0.75 watt).
- Pulsed Sending Data: sends packets of data at a distinct time.

---
General Information
General Information
Wireless Board:
- Uses SPI as main transfer method
- Synced with mainboard (pulsed sending as well)
- Sends data as raw ASCII text

---
Transceiver: Version 1.0
Transceiver: Version 1.0
Simplest Wireless Implementation
Mainboard Turns On
Mainboard sends data through wireless to pit
Mainboard goes into standby mode

---
Version 1.0: Pulse Cycle
Version 1.0: Pulse Cycle
One pulse cycle for Simplest Implementation
Active(of Transceiver)
Tsend
Time

---
Problems that Arise
Problems that Arise
This model does not allow for pit to sent any information to the car.
To combat this issue, we introduce version 2.0, a more complex variation that allows for two directional data transfer.

---
Transceiver: Version 2.0
Transceiver: Version 2.0
Mainboard
Powers On
Mainboard sends data through wireless board to the pit
Wait for a response from pit
Yes, request to send data
No Send Request
Mainboard goes into Standby Mode
Extends wait cycle to receive data
Receives and reads data from the pit

---
Version 2.0
Version 2.0
Handling Data Reception:
Data reception will end when either:
1. A threshold cycle time has been met
2. A end of message instruction was sent by the pit

---
 Textend and receive 
Active
 Twait 
 Tsend 
Time

---
Problems that Arise
Problems that Arise
Unhandled Failure of Data Transfer from Mainboard to the Pit
Two Types:
- Time Out
- Confirmed Failure from Pit

---
Transceiver Version 3.0
Transceiver Version 3.0
Mainboard Powers On
Mainboard Sends Data
Mainboard waits for response
Response: Successful Transmission
Response:
Failed Transmission
Response: Send Request
Extends Active Time
Saves current packet of data to be sent next time.
Receive Data from Pit
Data Response:
Failed Transmission
Data Response: Successful Transmission
Mainboard goes into standby mode

---
 Textend and receive 
This time also saves the data packets if the pit responds with a failure message
Active
 Twait 
 Tsend 
Time

---
Display Wireless(Mini wireless)
Display Wireless(Mini wireless)
The display and the motherboard are no longer connected this time around. All display operations are transferred wirelessly from the mainboard to the display.

---
Display Wireless
Display Wireless
??? What drains the battery? Main board or wireless, because why is mainboard always on for mini wireless???
The mainboard sends necessary data to the display, which is always on and listening for instructions.

---
Mainboard Flowchart
Mainboard Flowchart
Mainboard performs calculations and operations.
Twait is over
Data to send
Data send complete
Send

---
Display Flowchart
Display Flowchart
Perform Display Operations
Receives Interrupt command indicating new data arriving
Listen and Receive Data
Interrupt Complete

---
Mini Wireless Operations Chart
Mini Wireless Operations Chart
Listen to Mainboard instructions
Have a Message to Send
No
Was previous sent message successful?
Send Previous Message
Yes
Message Failed
Send Message
Saves data packet to be sent again
Wait for Response from Display
Message Successful
Mainboard power off